ANALYSIS OF ELASTIC FLEXURAL WAVES IN NON-UNIFORM BEAMS BASED ON MEASUREMENT OF STRAINS AND ACCELERATIONS

# L. Hillström and B. Lundberg

# The Ångström Laboratory, Uppsala University, Box 534, SE-751 21 Uppsala, Sweden

Elastic flexural waves in an unloaded and unsupported segment of a non-uniform beam were considered. A method based on Timoshenko’s model was established for evaluation of shear force, transverse velocity, bending moment and angular velocity at an arbitrary section from four independent measurements of such quantities at one to four sections. From the evaluated quantities, shear stress, normal stress, power transmission, etc. can be obtained. Experimental tests were carried out with an aluminium beam which had an abrupt change in height from 15 to 20 mm and was equipped with strain gauges and accelerometers at four uniformly distributed measurement sections and at three evaluation sections. The distance between the two outermost measurement sections was 600 mm, corresponding to 1.12 wave lengths at the upper end of the frequency interval 2-500 Hz considered. Bending moments and transverse velocities evaluated from four measurements of any one of these quantities agreed well with those measured at evaluation sections located (i) centrally among the measurement sections and (ii) at a distance of 100 mm, or 0.17 wave lengths, outside. When it was located (iii) at a distance of 500 mm, or 0.83 wave lengths, outside, there was relatively large disagreement as expected from error analysis.

# INTRODUCTION

Generation of elastic flexural waves in beams occurs in different technological processes, often as a side effect. In percussive drilling of rock, e.g., use is made of elastic extensional waves, but due to eccentric impacts, drill rods that are not perfectly straight [1], unsymmetrical loading of the drill bit [2], etc., flexural waves are also generated. This gives rise to, e.g., leakage of energy from the extensional waves, increased stress levels and increased generation of noise. If the predominant wavelengths are at least of the order of the transverse dimensions of the beam, the motion of flexural waves can be examined by using the Timoshenko beam model. If they are much longer, the wave motion can be studied also by using the Euler-Bernoulli beam model [3].

In various applications, and for different purposes, it is interesting to know the histories of shear force, transverse velocity, bending moment and angular velocity associated with flexural waves at one or several sections of a beam. From them, histories of other important quantities such as shear stress, deflection, normal stress, rotation of a cross-section and power transmission can also be determined.

For elastic extensional waves, Lundberg and Henchoz [4] showed that histories of normal force and particle velocity at an arbitrary section E of a uniform bar can be evaluated from measured strains at two different sections A and B by solving time-domain difference equations which are exact in relation to the one-dimensional theory used. A similar method was used by Yanagihara [5] to determine impact force. Lagerkvist and Lundberg [6], Lagerkvist and Sundin [7] and Sundin [8] used the method to determine mechanical point impedance. The method was used also by Karlsson et al. [9] in a study of the interaction of rock and bit in percussive drilling. It was extended to non-uniform bars by Lundberg et al. [10], and this version of the method was used for determination of force-displacement relationships for different combinations of drill bits and rocks by Carlsson et al. [11] and for high-temperature fracture mechanics testing by Bacon et al. [12, 13]. The use of the method was extended to visco-elastic extensional waves by Bacon [14, 15].

The aim of the present paper is to develop a method for evaluation of the histories of shear force, transverse velocity, bending moment and angular velocity at an arbitrary section E of a non-uniform beam from measurements of such quantities at different sections A, B, C and D. It will be shown that, for an unloaded segment of the beam, this can be achieved through measurement of altogether four such quantities which differ from each other in terms of either section (A, B, C and D) or type of quantity (shear force, transverse velocity, bending moment and angular velocity), or both.

First, the method will be developed on the basis of Timoshenko’s beam model. Then, experimental impact tests with a non-uniform beam made of aluminium and equipped with strain gauges and accelerometers will be presented, and comparisons will be made between (i) bending moments and particle velocities evaluated at section E on the basis of measurements at sections A-D and (ii) the same quantities measured at section E.

# THEoretical basis

## FORMULATION OF THE PROBLEM

Consider a segment of a non-uniform Timoshenko beam with cross-sectional area , moment of inertia , Young’s modulus , shear modulus  and density , where  is a co-ordinate along the straight centre line of the beam. For a rectangular cross-section, as in the experimental part,  and , where  is the width and  is the height. The shear modulus is related to the Young’s modulus by the relation , where  is Poisson’s ratio. Within the beam segment, there must be no loads, supports, joints or spots of contact. Outside, where there are no such restrictions, the beam is assumed to interact with supports, structures and loads. The supports and structures may have linear or non-linear responses, and they are assumed to have the capability to absorb energy associated with vibrations. Furthermore, the loads are assumed to act during finite time. Otherwise, nothing needs to be known about supports, structures or loads outside the beam segment under consideration.

The beam is quiescent for time , and for  it is subjected to a transverse load with finite duration. As a consequence, there will be a deflection of centre-line  and a rotation of cross-section . In the beam segment considered, these deflections and rotations are governed by the equations of motion

,     ,	(1)

respectively, where  is the transverse shear force and  is the bending moment.

The deflections and rotations are related to each other through the compatibility-type relation

,	(2)

where  is the shear strain on the centre-line, see Figure 1. The terms  and  on the right-hand side represent the contributions to the slope of the centre-line of the beam from bending and shear, respectively, and they are related to the bending moment and the transverse shear force through the constitutive-type relations

,     ,	(3)

where  is a dimensionless quantity which depends on the shear stress distribution and therefore on the shape of the cross-section. According to beam theory, this quantity can be determined from the relation , where the static moment  and in general also the width  depend on the vertical co-ordinate  from the centre-line. For a rectangular cross-section, this formula gives , which is the value to be used in the experimental part. According to another definition,  may depend also on Poisson’s ratio.

Equations (1) - (3) provide five relations between the five unknown functions , , ,  and . Through elimination, these relations can be transformed into, e.g., a system of two second-order partial differential equations (PDEs) for  and  or into a single fourth-order PDE for . Here, it will be more convenient to consider the system of four first-order PDEs

,     ,     ,     	(4)

for the four quantities , ,  and , which is obtained by eliminating  from equations (1) - (3). These quantities constitute the elements of a state vector , which is zero for . Furthermore, because of the energy-absorbing agents outside the beam segment,  as .

The problem to be solved is as follows. Consider the four elements , ,  and  of the state vector  at four different sections A, B, C and D of the beam segment, i.e., altogether sixteen elements. Let four out of them, constituting the elements of a vector , be known from measurements for . Then, determine the state vector  or its Fourier transform  (which is assumed to exist) at any section E of the beam segment. See Figure 2, where it is indicated that the variation of the geometrical and material properties along the beam segment may be continuous or discontinuous.

## SOLUTION IN THE GENERAL CASE

Fourier transformation of relations (4) gives

,	(5)

where

(6)

is the system matrix,

(7)

is the Fourier transform of the state vector , i.e., , and .

The state at any section  is related to that at the fixed section  through

.	(8)

Here, by equations (5) and (8), the transition matrix  satisfies

,     ,	(9)

where  is the identity matrix. In particular, equation (8), with  and with , , ,  and , gives

,     ,     ,     	(10)

for the segments AA, BA, CA and DA, and

(11)

for the segment EA. In equation (10a) it should be noted that .

The problem of determining the state vector  from knowledge of four out of the sixteen elements of the state vectors , ,  and  can now be solved as follows. First, four scalar equations, with linear combinations of the elements of  in their left-hand members and the measured elements of , ,  or  in their right-hand members, are singled out from the twelve scalar equations represented by equations (10). They form a system of four linear equations for the four elements of  which can, at least in principle, be solved uniquely if the determinant of this system is different from zero. Then, with  known,  is determined from equation (11). It should be noted that the physical order of sections A-E along the beam must not be alphabetical and also that all sections A-D must not be involved in the measurements.

As a first illustration, consider measurement of the bending moment  at each section A-D. In this case, the third scalar equation from each of the matrix equations (10) give the system

,	(12)

where subscript m denotes measurement. It can also be written

.	(13)

As , the first row of the matrix on the left-hand side is , which gives the trivial relation  or .

As a second illustration, consider measurement of the transverse velocity  at each section A-D. In this case, the second scalar equation from each of the matrix equations (10) give the system

,	(14)

which can also be written

.	(15)

As , the first row of the matrix on the left-hand side is , which leads to the trivial relation  or .

In the general case, equations (13) and (15) take the form

(16)

or

,	(17)

where

,     .	(18)

Here  is a matrix with elements  singled out from the transition matrices , ,  and , and  is a vector with elements  of measured quantities at different sections of the beam ( and 1, 2, 3 or 4). The subscript 1, 2, 3 or 4 defines the type of quantity (, ,  or , respectively) and the superscript  A, B, C or D the section associated with . These quantities, which can be considered to be the elements of vectors  and , respectively, define the measurements.

Equations (11) and (17) give the state vector

,	(19)

in terms of the vector  of measured quantities. Transformation into the time domain gives the state vector  for . This solves the stated problem.

If there is an error  in , it follows that there will be a corresponding error

(20)

in . On the element level, an error  in the evaluated quantity , due to an error  in the measured quantity , can be expressed . Comparison with equation (20) shows that the derivative  can be obtained as the element  of the matrix . The absolute value of this derivative will be used as a measure of the sensitivity of the evaluated quantity  to an error in the measured quantity .

## BEAM WITH PIECEWISE CONSTANT PROPERTIES

If the beam has piecewise constant properties as indicated in Figure 3, the transition matrices in equations (10b-d) and (11) can be expressed as the products

,     ,     ,     	(21)

and

,	(22)

respectively, of transition matrices , ,...,  for beam elements with constant properties. These matrices, in turn, can be determined by first solving the problem (9) for matrices  which are independent of , and then substituting appropriate values for  and . In this case, the coupled problem (9) for the elements of  can be replaced by an uncoupled problem as follows.

For  independent of , equation (9a) gives

,     ,     ,     .	(23)

The eigenvalues  of the matrix  are given by the four roots of , i.e., with use of definition (6),

,	(24)

where

,     .	(25)

Thus, there are the two pairs of eigenvalues

,     ,	(26)

where

,     	(27)

are both real and positive provided that

,	(28)

which is presumed. According to Cayley-Hamilton’s theorem, equation (24) for the eigenvalues of the matrix  is satisfied also by , i.e.,

.	(29)

Multiplication by  from the right and use of relations (23b, d) gives the fourth-order differential equation

.	(30a)

Furthermore, relations (9b) and (23a-c) give the conditions

,	(30b)

,     ,     	(30c-e)

for . Thus, the coupled problem (9) for the elements of  has been replaced by the uncoupled problem (30), which has the solution

(31)

with

,     ,	(32a, b)

,     	(32c, d)

# EXPERIMENtal tests

The experimental set-up is illustrated in Figure 4. A beam made of aluminium (AA 6061-T6;  GPa,  and  kg/) with rectangular cross-section and length 2250 mm was used. The width  of the beam was 20 mm, while its height  was 15 mm in the central third and 20 mm in the two outer thirds. The beam was held in position by three supports with positions as shown. Each of these supports was realised with a pair of 15 mm wide clamps clad with 1.5 mm thick rubber plates. The beam was impacted laterally by a spherical steel ball which was guided by a tube and dropped from a height of 600 mm. The diameter of the ball was 50 mm, and its mass was 535 g. A 3 mm thick rubber plate at the impacted spot of the beam served to reduce the excitation at high frequencies.

The beam was instrumented with strain gauges and accelerometers at the sections A-D and - as shown in Figure 4. The positions of the strain gauges coincided with these sections, while those of the accelerometers were displaced 20 mm to the right, i.e., away from the spot of impact. The strain gauges (TML FLA-5-23-1L) were glued (Tokyo Sokki Kenkyujo Co, Ltd, Adhesive CN) to the beam in pairs with one on the top and one on the bottom. The gauges of each pair were connected to a bridge amplifier (Measurement Group 2210) in opposite branches, so that the output of the amplifier was proportional to the difference between the two strains, and therefore to the bending moment  at the section. Shunt calibration was used. Accelerometers (Brüel & Kjær, three Type 4374 and two Type 4393) were attached with thin layers of wax. The accelerometers were connected to charge amplifiers (three Kistler Type 5011 and two Brüel & Kjær Type 2635). Ideally, there should have been one type of accelerometer and one type of charge amplifier only, but it was judged that the use of different types would not have any noticeable effect upon the results.

The amplified strain and accelerometer signals were fed to analogue aliasing filters (DIFA Measuring Systems, PDF) with cut-off frequency 17.5 kHz. The filtered signals were recorded in a time interval , with  s, by two synchronised four-channel digital oscilloscopes (Nicolet Pro 20 and Pro 40) which used a sampling interval of 20 s. At the end of this time interval, the amplitudes of the recorded signals were reduced to about a tenth due to the damping action of the supports. The recorded signals were transferred to a computer for evaluation of the state vector . First, measured accelerations, if any, were integrated to velocities. After use of the FFT algorithm,  was determined according to equation (19). Finally,  was transformed into the time domain by use of the inverse FFT algorithm. Results were produced for the same time interval  even though sometimes they may be valid only in a narrower interval . When, e.g., section E is located outside AD, as in some of the experimental tests, there must clearly be a certain difference between  and  which is related to the travel times for flexural waves from section E to sections A-D.

Four test cases, labelled 1 - 4, are defined in Table 1. In Case 1, bending moments  at sections A-D (, ) and - were determined from measurements of strains at the same sections. In Case 2, bending moments  at sections A-D and transverse velocities  at - were determined from measurements of strains and accelerations, respectively, at the same sections. In Case 3, transverse velocities  at sections A-D (, ) and  were determined from measurements of accelerations at the same sections. In Case 4, finally, transverse velocities  at sections A-D and bending moment  at  were determined from measured accelerations and strains, respectively, at the same sections. In this case, the signals representing accelerations and strains were passed through 8-pole Butterworth high-pass filters with cut-off frequency 10 Hz. In each of the four cases, bending moments  or transverse velocities  at sections -, corresponding to the measurements made at these sections, were also determined from those measured at A-D according to equation (19). All tests were carried out at room temperature.

# RESULTS

Figure 5 shows for Case 1 the sensitivity  of the bending moment  to an error in the bending moment  as a function of the position  of section E and of the frequency . It can be seen that the sensitivity to error is unity or less if the position  is not too far outside the interval [] and if the frequency is not too high. In particular, the sensitivity to error is zero if ,  or , and it is unity if . It should also be noted that the sensitivity to error is very high around a frequency of approximately 850 Hz. Similar results were obtained for other cases and other sensitivities.

Figure 6 shows results in the time and frequency domains at section  for Case 1. In Figure 6(a), the results in the time domain are based on frequencies up to 500 Hz, which means that frequencies around 850 Hz are excluded, while in Figure 6(b) they are based on frequencies up to 2000 Hz. Evidently, there is a significantly better agreement between evaluated and measured bending moments in the former case. For this reason, the results for Cases 1-4 shown in Figures 7-10 are based on frequencies up to 500 Hz.

# DISCUSSION

It has been shown how the elements , ,  and  of the state vector  at any section E of an unloaded segment of a non-uniform beam can be determined from measurement of four such elements at up to four different sections A, B, C and D of the same unloaded segment of the beam. This has also been demonstrated experimentally. Once the state vector has been determined, several quantities of importance can be obtained from its elements. Thus, e.g., the shear stress  can be obtained from , the normal stress  from , the deflection  from , and the rotation of the cross-section  from . Also, the power transmission can be obtained from the relation . It should be emphasized that nothing needs to be known about supports, structures and loads outside the beam segment under consideration.

The combination of sections, among A, B, C and D, and types of quantities to be measured, among , ,  and , can be chosen in a large number of ways, some of which may be more interesting than others. Thus, it is convenient to determine bending moment  from measured strains and transverse velocity  from measured accelerations, as was done in the experimental part, while it is less straightforward to determine  or  from measurements. Also, it seems preferable to place at most two types of transducers at any section A-D of the beam, and to make the same kind of measurement or measurements at each instrumented section. Therefore, two interesting possibilities are measurement of (i)  at each section A-D (Cases 1-2) and (ii)  at each section A-D (Cases 3-4), as in the experimental part. A third interesting possibility would be measurement of (iii) both  and  at each of two sections, e.g., A and B. It should also be noted, that a free end, say A, with  and  can be used to replace two measurements. Other types of homogeneous boundary conditions generally represent real situations less accurately.

The functions  and  introduced in equations (26) and (27) can be interpreted as follows. Let the state vector have the form . Then, substitution into equation (5) gives the eigenvalue problem . The eigenvalues  are given by the four roots of , i.e., the four roots of equation (24) with . Thus, according to equation (26), the eigenvalues are  and . Therefore, provided that the condition (28) is satisfied as presumed,  determines the decay of non-propagating disturbances and  is the wave number of propagating harmonic waves ().

For radian frequencies , where  is the speed of elastic extensional waves and  is the radius of inertia of the cross-section, equations (27) can be approximated by  and equation (25b) by . As by definition the wave number  is related to the wave length  by , one obtains  with . In terms of the frequency  and the height  of a beam with rectangular cross section, the corresponding relations are , , and , with . These approximations of  and  at low frequencies represent the limiting case of the Euler-Bernoulli beam.

For the aluminium beam used in the experimental tests, the highest frequency normally considered, 500 Hz, corresponds to the wavelengths 0.606 m and 0.525 m in the segments with heights 20 mm and 15 mm, respectively. Similarly, the frequency 2000 Hz, considered in Figure 6 only, corresponds to the wavelengths 0.300 m and 0.260 m, respectively. Thus, in the tests carried out the wavelengths were much larger than the heights of the beam, and . This means that the above approximations are accurate and also that the condition (28), which can be written in the form, is satisfied.

The determination of errors at section E due to errors of measurement, including noise, at one or several of sections A-D according to relation (20) can be split into the two steps (i) , which gives errors at section A in terms of errors of measurement, and (ii) , which gives errors at E in terms of errors at A. In the time domain, these steps correspond to a deconvolution and a convolution, respectively. Under certain conditions, each of them may generate large errors. Such conditions are related to the matrices -, which determine the elements of the matrix , and to the matrix . For the discussion which follows it is useful to note from equation (31) that, in the special case of a uniform beam and for relatively low frequencies with , these matrices contain terms proportional to , , ..., and , respectively.

In the first step, which involves inversion of the matrix , the error  may become large if the matrix  is ill-conditioned. In the case represented by equation (12), this may occur at low frequencies corresponding to long wave lengths which make the four scalar equations nearly the same. It may also occur at high frequencies corresponding to short wave lengths which make the magnitudes of the elements in the different rows of the matrix  very different. Thus, e.g., the ratio of the exponential factors of the fourth row in equation (12) to those of the first row is , which may be very large even for modest ratios . In the experimental tests, the distance AD (600 mm) was slightly longer than one wave length () at the highest frequency 500 Hz which corresponds to the ratio . The matrix  may be ill-conditioned also near discrete frequencies which make several distances between adjacent sections A-D equal to an integral multiple of a half wave length. In Case 1, the distances AB and BC in the thinner central section of the beam are one half wave length at a frequency of about 860 Hz which may explain the high sensitivity to errors around 850 Hz illustrated in Figure 5. This problem was avoided in the experimental tests by only considering frequencies below 500 Hz.

The effects of noise in the measured data may be reduced by use of Wiener filtering techniques [16]. Also, a conceivable way of avoiding integral multiples of half wave lengths between adjacent sections A-D, which might allow frequencies considerably higher than 500 Hz, would be to make use of more than four measurements, so that the system (17) for the elements of  would be over-determined, and of a non-uniform distribution of instrumented sections. This way of eliminating critical frequencies has been found to be effective in an application involving viscoelastic extensional waves [17].

In the second step, which involves multiplication of the error  at section A with the matrix , the error  may become large if the exponential factor  is very large. This occurs if the distance AE is large. In the experimental tests the distances ,  and  were approximately 0.57, 1.28 and 1.94 wave lengths at the highest frequency 500 Hz. Thus,  was located at the centre of the beam segment AD, while  and  were located at distances 0.16 and 0.82 wave lengths, respectively, outside this segment. The corresponding exponential factors were ,  and , respectively.

For Case 1, Figure 7 shows that there is excellent agreement in the frequency range 2-500 Hz between (i) the bending moment evaluated at section  from measurements of bending moments at sections A-D and (ii) the bending moment measured at the same section . For section  the agreement is very good in the same range of frequencies. For section  there is relatively large disagreement, in particular at high frequencies, corresponding to short wave lengths and large exponential factors , and in the time domain near  s.

For Case 2, Figure 8 shows that there is good agreement in the frequency range 10-500 Hz between (i) the transverse velocity evaluated at section  from measurements of bending moments at sections A-D and (ii) the transverse velocity measured at the same section . For section  the agreement is fair in the same range of frequencies. For section  there is again relatively large disagreement, in particular at high frequencies, corresponding to short wave lengths and large exponential factors , and in the time domain near .

Cases 1 and 2 show that the quality of the evaluated results is generally high when section E is located within the segment AD, whereas it rapidly decays outside. This is consistent with the rapid increase in sensitivity to errors outside the segment AD shown in Figure 5 for Case 1. The large disagreement near  s for section  in both cases is believed to be due to the difference between  and  which was mentioned in the experimental part. Thus, where the large errors occur, information from section  may not yet have reached sections A-D to the extent required. This error can be avoided by recording signals till all waves are damped out. Then,  and  can be considered to be arbitrarily large.

For Case 3, Figure 9 shows that there is a fair agreement in the frequency range 20-500 Hz between (i) the transverse velocity evaluated at section  from measurements of transverse velocities at sections A-D and (ii) the transverse velocity measured at the same section . For Case 4, Figure 10 shows that there is a fair agreement in the same range of frequencies between (i) the bending moment evaluated at section  from measurements of transverse velocities at sections A-D and (ii) the bending moment measured at the same section .

It should be noted that the accelerometers used are quite inaccurate below 10 Hz. This inaccuracy is reflected by the disagreement between evaluated and measured quantities below 10-20 Hz in Cases 2-4. The fair agreement in Case 4 was obtained by using the Butterworth high-pass filters which reduced this disagreement.

Comparison of Figures 7(b) and 10 shows that the bending moment evaluated at section  is more accurate if the evaluation is based on measured bending moments at sections A-D than on measured transverse velocities. Similarly, comparison of Figures 8(b) and 9 shows that the transverse velocity evaluated at section  is more accurate if the evaluation is based on measured transverse velocities at A-D than on measured bending moments. This is partly explained by Figure 6 which shows that when the quantity evaluated at E is the same as that measured at A-D, the sensitivity to errors is relatively low within and near the segment AD of the beam. This is not necessarily the case when the quantity evaluated at E is different from that (or those) measured at A-D.

The method of this paper makes use of transition matrices which relate the state vectors at the two ends of a beam element. It would be possible, as an alternative, to make use of the corresponding dynamic stiffness matrices which relate the generalised forces to the generalised velocities at the two ends of the beam element. For the beam segment considered, this approach would result in a system , where  is the dynamic stiffness matrix,  is the nodal generalised velocity vector, and  is the nodal generalised load vector. If the number of nodes of the beam segment considered would be , corresponding to  beam elements, the matrix  would be  and the vector  would contain  generalised velocities ( velocities and  angular velocities). Also, the vector  would contain four nodal generalised forces (one transverse shear force and one bending moment at each end node of the beam segment considered) in addition to zeroes. Thus, there would be a system of  relations between  generalised velocities and forces. If four of these quantities are measured, the system  can generally be solved for the remaining ones. Although there may be differences in ease of establishing the system to be solved, in ease of obtaining the desired elements of the state vector, in ease of interpretation of the wave phenomena involved, in computational efficiency, etc., it should be emphasised that the approaches involving transition matrices and dynamic stiffness matrices are equivalent.

ACKNOWLEDGEMENTS

Funding of this research from the Carl Trygger Foundation, the Swedish Council for Engineering Sciences and AB Sandvik Tamrock Tools is gratefully acknowledged.

# REFERENCES

1.	R. Beccu, C.M. Wu and B. Lundberg 1996 Journal of Sound and Vibration 191(2), 261-272. Reflection and transmission of the energy of transient elastic extensional waves in a bent bar.

2.	I. Carlvik 1981 Int. J. Rock Mech. Min. Sci. & Geomech. Abstr. 10, 167-172. The generation of bending vibrations in drill rods.

3.	K. F. Graff 1975 Wave motion in elastic solids. Mineola, New York: Dover Publications, Reprinted edition, 1991.

4.	B. Lundberg and A. Henchoz 1977 Experimental Mechanics 17(6), 213-218. Analysis of elastic waves from two-point strain measurement.

5.	N. Yanagihara 1978 Bulletin of the Japan Society of Mechanical Engineers 21, 1085-1088. New measuring method of impact force.

6.	L. Lagerkvist and B. Lundberg 1982 Journal of Sound and Vibration 80, 389-399. Mechanical impedance gauge based on measurement of strains on a vibrating rod.

7.	L. Lagerkvist and K.G. Sundin 1982 Journal of Sound and Vibration 85, 473-481. Experimental determination of mechanical impedance through strain measurement on a conical rod.

8.	K.G. Sundin 1985 Journal of Sound and Vibration 102, 259-268. Performance test of a mechanical impedance gauge based on strain measurement on a rod.

9.	L.G. Karlsson, B. Lundberg and K.G. Sundin 1989 Int. J. Rock Mech. Min. Sci. & Geomech. Abstr. 26, 45-50. Experimental study of a percussive process for rock fragmentation.

10.	B. Lundberg, J. Carlsson and K. G. Sundin 1990 Journal of Sound and Vibration 137(3), 483-493. Analysis of elastic waves in non-uniform rods from two-point strain measurement.

11.	J. Carlsson, K. G. Sundin and B. Lundberg 1990 Int. J. Rock Mech. Min. Sci. & Geomech. Abstr. 27(6), 553-558. A method for determination of in-hole dynamic force-penetration data from two-point strain measurement on a percussive drill rod.

12.	C. Bacon, J. Carlsson and J. L. Lataillade 1991 Journal de Physique III (Suppl., Colloque C3) 1, 395-402. Evaluation of force and particle velocity at the heated end of a rod subjected to impact loading.

13.	C. Bacon, J. Färm and J. L. Lataillade 1994 Experimental Mechanics 34(3), 217-223. Dynamic fracture toughness determined from load-point displacement on a three-point bend specimen using a modified Hopkinson pressure bar.

14.	C. Bacon 1998 Experimental Mechanics 38(4), 242-249. An experimental method for considering dispersion and attenuation in a viscoelastic Hopkinson bar.

15.	C. Bacon 1999 International Journal of Impact Engineering 22(1), 55-69. Separation of waves propagating in an elastic or viscoelastic Hopkinson pressure bar with three-dimensional effects.

16.	T. Söderström 1994 Discrete stochastic systems. Estimation and control. Cambridge: Prentice Hall International (UK) Limited 1994.

17.	L. Hillström, M. Mossberg and B. Lundberg 2000 Journal of Sound and Vibration 230(3), 689-707. Identification of complex modulus from measured strains on an axially impacted bar using least squares.

TABLES

Table 1. Cases of experimental tests.

| Case |  | Input |  | Output |  | High-pass |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | A-D |  |  |  |  |  | filter |
| 1 |  |  |  |  |  |  |  | no |
| 2 |  |  |  |  |  |  |  | no |
| 3 |  |  |  | - |  | - |  | no |
| 4 |  |  |  | - |  | - |  | yes |

FIGURES

Figure 1.	Angles , , , shear force , transverse velocity , bending moment  and angular velocity  at a general section  of the beam.

Figure 2.	Unloaded section of non-uniform beam in the general case. Sections of measurement A-D and of evaluation E.

Figure 3.	Unloaded section of beam with piece-wise constant properties. Sections of measurement A-D and of evaluation E.

Figure 4.	Experimental set-up. Dimensions in mm.

Figure 5.	Sensitivity  of bending moment  to error in bending moment  vs. position  and frequency  in Case 1. (a) 100 Hz  600 Hz and (b) 500 Hz  1000 Hz.

Figure 6.	Bending moment  vs. time  and  vs. frequency . Comparison between bending moment at  evaluated from bending moments measured at A-D (solid curves) and bending moment measured at  (dotted curves) in Case 1. Results for frequencies up to (a) 500 Hz and (b) 2000 Hz.

Figure 7.	Bending moments (a)  vs. time  and  vs. frequency , (b)  vs. time  and  vs. frequency , and (c)  vs. time  and  vs. frequency . Comparison between bending moments at - evaluated from bending moments measured at A-D (solid curves) and bending moment measured at - (dotted curves) in Case 1. Results for frequencies up to 500 Hz.

Figure 8.	Transverse velocities (a)  vs. time  and  vs. frequency , (b)  vs. time  and  vs. frequency , and (c)  vs. time  and  vs. frequency . Comparison between transverse velocities at - evaluated from bending moments measured at A-D (solid curves) and transverse velocities measured at - (dotted curves) in Case 2. Results for frequencies up to 500 Hz.

Figure 9.	Transverse velocity  vs. time  and  vs. frequency . Comparison between transverse velocity at  evaluated from transverse velocities measured at A-D (solid curves) and transverse velocity measured at  (dotted curves) in Case 3. Results for frequencies up to 500 Hz.

Figure 10.	Bending moment  vs. time  and  vs. frequency . Comparison between bending moment evaluated at  from transverse velocities measured at A-D (solid curves) and bending moment measured at  (dotted curves) in Case 4. Results for frequencies up to 500 Hz.