## Slide 1: “It's a Trap!”-How Speculation Invariance Can Be Abused with Forward Speculative Interference
Pavlos Aimoniotis
Christos Sakalis
Magnus Själander (@ NTNU)
Stefanos Kaxiras

## Slide 2: What I’m going to tell you:
Lifting defenses from speculative-invariant instructions is dangerous!
In this talk:
  Speculative defenses: e.g.: delay-on-miss (DoM)
  Speculative invariance: lifting these defenses for bound-to-commit instructions
  Speculative interference: speculative instructions interfering with non-speculative instructions OR …
  …. interfering with bound-to-commit instructions using a novel side-channel (ROB contention)
  Demonstrate ROB contention on unprotected cores
  Propose ways to address problem (WIP)
{
Our contributions
Notes: (instructions that are bound-to-commit regardless of the outcome of speculation)
Because: speculative instructions can interfere with the bound-to-commit instructions and reveal through this interference the secret

## Slide 3: Delay-on-Miss
Delays transient loads until they become non-speculative
  Delays only loads that miss in the cache
  Allows hits in L1 Cache to execute under speculation
  Delays any side-effects until load becomes non-speculative
Defenses with similar goals: Invisispec [MICRO'18], GhostLoads [CF'19], Muontrap [ISCA'20], etc.
Question: can we lift these defenses while in speculation?

## Slide 4: Speculation Invariance
Zhao et al. insight: we can lift such defenses for bound-to-commit instructions that are independent to the outcome of speculation
  InvarSpec: Framework that detects speculation invariant instructions
    Statically determines dependences through compiler
    At runtime hardware lifts protection for speculation invariant instructions
Not entirely true …
Notes: However, not entirely true! because speculation instr can interfere with the bound-to-commit instr
What is inteference?

## Slide 5: Speculative Interference Attacks
Break defense mechanisms like DoM and Invisispec
By influencing ordering of memory operations:
“Backward” SI because younger speculative instructions interfere with older non-speculative instructions
interference_target;
if() {// mispredict
ld secret // hit
interference_gadget(secret);
}
“Backward”

## Slide 6: Our contribution: Forward SI
Older speculative instructions interfere with younger bound-to-commit instructions:
ROB contention
if() {
ld secret // hit
interference_gadget(secret);
}
interference_target;
“Forward”

## Slide 7
train_branch_predictor();
if() { // mispredict
ld secret // hit
if(secret){
fill_the_ROB;
}
else
{} // nothing
}
else { // correct path
time();
load A;
time();
}
load A // bound-to-commit spec-invar
Secret
Depend.
1
0
1
0
ROB Contention?
Tight loop or long sequence of spurious instructions
Single static instruction
  x86 ISA REP instruction: expands speculatively
ROB-Empty
ROB-Contention
meas.
ld A
ld A
ROB
if()
ld A
ld A
No entry available.
Does not execute and
thus not brought in cache!
Available entry.
Executes and brought to cache!
Hit? Secret == 0!
Miss? Secret == 1!

## Slide 8: Expiremental Results
Speculation invariant instructions that lift protections are equivelant to bound-to-commit instructions on real core!
  Have the same behaviour
Delaying with a for-loop
  avg load on delay path 258 cycles (miss)
  avg load on fast path equals 73 cycles (hit)
Delaying with REP
  avg load on delay equals path 260 cycles (miss)
  avg load on fast path equals 170 cycles (hit)
System
  Intel Core i7-2600k, Sandy Bridge, 3.40GHz
  4 Cores, 3 Cache levels
    32KiB L1 Cache, 256KiB L2 Cache, 8MiB Shared-LLC
Notes: [Interpret the results  spec-invariant become transmitters!]
STRONG SIGNAL TO DISTINGUISH THE SECRET

## Slide 9: Future Work - Forward Speculative Interference Mitigations
Do not lift protections if branch paths differ under speculation!
Balance the paths
Make speculative ROB-filling operand-independent
  Similar to Yu, Jiyong, et al. "Speculative data-oblivious execution: Mobilizing safe prediction for safe and efficient speculative execution." (ISCA '20)

## Slide 10: Conclusion
Side-channel based on ROB contention
Speculative Interference
  Forward SI
Selectively lifting protections is vulnerable
Proposed a number of mitigations

## Slide 11: Thank you!